## Slide 1: Whither Acoherent Shared Memory?
Mark D. Hill
UW-Madison Computer Sciences
Workshop on Negative Outcomes, Post-mortems, and Experiences (NOPE)
December 2015

## Slide 2: Title/Abstract
Title: Whither Acoherent Shared Memory?
Speaker: Mark D. Hill, UW-Madison Computer Sciences
In 2012 we wrote: “Given the current trends in computing, including an increased focus on energy efficiency and a push towards more hardware specialization, now may be a good time to rethink coherent memory in multiprocessors. To this end, we present Acoherent Shared Memory (ASM), a new shared memory model which allows hardware and software to work together to manage data efficiently by exploiting semantic information. The keystone of ASM is a novel memory abstraction called acoherence that presents memory as a CVS-like repository to software. We show that the acoherent model, with the ability to check-out and check-in copies of memory, is a good semantic match for the majority of shared memory in a program and can lead to efficient hardware designs.”
While this work appears in Derek R. Hower’s 2012 Wisconsin Ph.D. thesis [http://www.cs.wisc.edu/multifacet/theses/derek_hower_phd.pdf], it was never successfully published. This short talk discusses possible reasons why.
Hower’s Ph.D. defense: http://www.cs.wisc.edu/multifacet/theses/derek_hower_phd_talk.pptx

## Slide 3: But NOPE Can Be Fun Too

## Slide 4: Acoherent Shared Memory
Derek R. Hower
Ph.D. Defense, July 16, 2012
www.cs.wisc.edu/multifacet/theses/derek_hower_phd.pdf
www.cs.wisc.edu/multifacet/theses/derek_hower_phd_talk.pptx

## Slide 5: Executive Summary & Outline
Acoherent Shared Memory [2012]
  Coherence is complex & inefficient
  Switch to CVS-like checkout/checkin model
  Same performance; less energy for CPUs
Whither Acoherent Shared Memory?
  CPUs coherence “settled”
  GPU/accelerators not ready
  Timing wrong; hard to publish out-there ideas
But seeded Heterogeneous Race Free

## Slide 6: The Big Picture
P
P
Coherent
View
P
P
CO
CO
CI
CI
Acoherent
View
GPU
Simple abstraction
?
L1
L1
L2
Simple abstraction
Simple implementation
Abstracts caches
Low overhead
- Complex implementation
Hides caches (bad?!)
High overhead
Notes: Coherence hides memory hierarchy. We may not want to do that going forward.
SW may want to use different memories. Coherence makes that difficult.

## Slide 7: The Problem With Coherence
Wrong abstraction
  Optimized for fine-grained, share-everything
    Programs aren’t!
  Makes SW isolation hard
  Hypothesis: SW will want control over data placement
Impedes HW specialization
  Does your multicore ASIC need a coherence controller?
  Coherent GPUs?
Efficiency problems
  Directories take space/broadcasts take energy
    e.g. 14% of cache are dedicated to directory on 4-core die1
1 Stackhouse et al., ISSCC 2008

## Slide 8: Rethinking Coherence: Goals
Maintain programmer sanity
  Keep shared memory
  Minimal compatibility change
Expose hardware capabilities
  Let SW guide memory management -> semantics
Simple hardware
  Lower cost of entry for accelerators
Solution: Acoherent Shared Memory

## Slide 9: ASM Model Basics
Replace black box with simple hierarchy
  Still flat, linear address space
  SW gets private storage
Manage with CVS-like checkout/checkin
P
CI
P
CI
CO
CO
Notes: Use small pictures for views

## Slide 10: Checkout/Checkin
Checkout:
Pull data into private storage
P
CI
P
CI
CO
CO
Checkin:
Publish local updates globally
Checkout/Checkin are
not synchronization primitives
- Closer to a FENCE
Granularity?
Notes: Checkouts are lazy

## Slide 11: Segments
Stack
Code
BSS
Data
Heap
Compromise: Memory Segments
  Linear partition of address space
  CO/CI segments at a time
Observation: Programs are already segmented
  Can re-use layout
Typical CO/CI granularity
in existing C code

## Slide 12: Segment Types
Acoherent
Private
Stack
Code
BSS
Data
Heap
Coherent RO
Shared
Private
Shared, Read-Only
Not all memory wants/needs acoherence
  Segment types give different “views”
  Communicate semantic information to HW
Available Types
Private
Coherent-RW
Coherent-RO
Acoherent
Device

## Slide 13: Managing Finite Resources
Model so far is strong acoherence
  Likely requires prohibitive HW resources
Also weak acoherence and best-effort acoherence
  Still useful to software/hardware
Weak acoherence:
  Data visible early (before checkin)
Best-effort acoherence:
  Spontaneous checkouts at any time
    + SW notification
  All-or-nothing
Synchronized =>
not a problem
Hybrid Runtimes =>
not a problem

## Slide 14: ASM-CMP Overview
Based on MIPS
  + special insns, e.g., checkout, checkin
  Uses segments, no paging
    Maintains flat address space
Coherence protocol -> Acoherence Engine
  DMA for caches
    Selectively move data
Skipping the Details

## Slide 15: Acoherence Engine
Three main responsibilities:
  Checkout:
    Invalidate all segment data
  Checkin:
    Write back all dirty segment data
  Order:
    Detect CI-CO pairs
FSM like coherence, but few races, no directory
Timestamp based
Lazy Flash Invalidate
Track write set
Decoupled
Metastate
Cache

## Slide 16: Performance
Chart: Runtime Normalized to MOESI
| barnes | fft | fmm | lu | mp3d | ocean | radix | water | cilksort | clu | heat2d | heat3d | matmul | uts_circ | uts_fixed | gmean
moesi | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
mesi | 0.99853 | 1.0041 | 1.0136 | 0.98864 | 0.62722 | 0.89728 | 1.0378 | 0.97168 | 0.95114 | 0.96157 | 1.1876 | 0.98693 | 0.92726 | 0.99539 | 1.0149 | 0.96351
asm | 1.0114 | 1.0056 | 1.078 | 1.0031 | 0.25478 | 0.96348 | 1.045 | 1.0076 | 0.99373 | 1.0859 | 1.0344 | 0.98818 | 1.0242 | 1.0002 | 1.0162 | 0.92808
Comparable performance
Checkout too much
False Sharing/
Migratory Sharing

## Slide 17: Energy
Chart: Energy Normalized to MOESI
| . | barnes | fft | fmm | lu | mp3d | ocean | radix | water | cilksort | clu | heat2d | heat3d | matmul | uts_circ | uts_fixed | gmean
e_l1d | 0.1256 | 0.12525 | 0.14044 | 0.17302 | 0.17282 | 0.19247 | 0.19283 | 0.19421 | 0.22221 | 0.11899 | 0.11686 | 0.13137 | 0.11556 | 0.076843 | 0.043628 | 0.13466 | 0.12384 | 0.14406 | 0.15265 | 0.15372 | 0.17147 | 0.15811 | 0.15533 | 0.17628 | 0.14844 | 0.14204 | 0.16063 | 0.12044 | 0.11535 | 0.14011 | 0.15055 | 0.16606 | 0.16916 | 0.15191 | 0.14815 | 0.16461 | 0.12053 | 0.11199 | 0.13394 | 0.17267 | 0.17091 | 0.18748 | 0.18297 | 0.18414 | 0.20439 | 0.14599 | 0.14018 | 0.15097
e_l1i | 0.10636 | 0.10608 | 0.10699 | 0.10787 | 0.10812 | 0.10734 | 0.11128 | 0.11253 | 0.11811 | 0.10209 | 0.10079 | 0.10024 | 0.10371 | 0.065429 | 0.027565 | 0.11273 | 0.10279 | 0.10693 | 0.10484 | 0.10723 | 0.10514 | 0.12695 | 0.12428 | 0.12722 | 0.11141 | 0.10594 | 0.10778 | 0.11256 | 0.1079 | 0.1194 | 0.10961 | 0.12615 | 0.10995 | 0.11253 | 0.10925 | 0.10787 | 0.10626 | 0.098205 | 0.1053 | 0.11494 | 0.11319 | 0.1135 | 0.1186 | 0.11978 | 0.11984 | 0.11062 | 0.10614 | 0.10106
e_l2 | 0.24855 | 0.24769 | 0.17714 | 0.22852 | 0.22671 | 0.16034 | 0.22522 | 0.22787 | 0.17261 | 0.24796 | 0.2426 | 0.17449 | 0.26055 | 0.15703 | 0.045054 | 0.23843 | 0.21064 | 0.16073 | 0.23065 | 0.23409 | 0.1673 | 0.23152 | 0.22426 | 0.16544 | 0.2337 | 0.21834 | 0.16244 | 0.24706 | 0.23667 | 0.19026 | 0.23307 | 0.27085 | 0.16637 | 0.2333 | 0.22785 | 0.16149 | 0.24376 | 0.22326 | 0.17527 | 0.2215 | 0.21651 | 0.15464 | 0.22547 | 0.2283 | 0.16193 | 0.23639 | 0.22484 | 0.1536
e_link | 0.24556 | 0.2452 | 0.25864 | 0.2218 | 0.22271 | 0.29083 | 0.22255 | 0.22557 | 0.2814 | 0.24016 | 0.23743 | 0.31337 | 0.24265 | 0.15219 | 0.087113 | 0.22949 | 0.20592 | 0.31496 | 0.21858 | 0.22685 | 0.38473 | 0.22839 | 0.22193 | 0.25587 | 0.22414 | 0.21319 | 0.32588 | 0.24346 | 0.2341 | 0.28997 | 0.22291 | 0.26473 | 0.35209 | 0.22725 | 0.22428 | 0.28346 | 0.23631 | 0.21912 | 0.31095 | 0.21313 | 0.21215 | 0.28833 | 0.22253 | 0.22585 | 0.24549 | 0.22906 | 0.2207 | 0.27418
e_switch | 0.27392 | 0.22864 | 0.19358 | 0.26879 | 0.22543 | 0.18549 | 0.24813 | 0.21123 | 0.19557 | 0.29081 | 0.2383 | 0.2007 | 0.27753 | 0.16154 | 0.053657 | 0.28469 | 0.21712 | 0.19107 | 0.29328 | 0.25335 | 0.20741 | 0.25503 | 0.20842 | 0.18687 | 0.28232 | 0.22937 | 0.19809 | 0.27649 | 0.22586 | 0.21643 | 0.28386 | 0.28048 | 0.20255 | 0.275 | 0.22479 | 0.18488 | 0.29313 | 0.21916 | 0.20431 | 0.27775 | 0.2109 | 0.18125 | 0.25043 | 0.21215 | 0.18024 | 0.27505 | 0.22172 | 0.1786
e_tlb | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Less Energy
(Same Performance)

## Slide 18: Related Work – ASM Model
Relaxed consistency models
  Release Consistency (ISCA 1990)
    Acquire/Release ≈ CO/CI
  DRF-0 (ISCA 1990), DRF-1 (PDS 1993)
    SC for DRF
  Weak ordering (ISCA 1998)
Semantic Segmentation
  Cohesion (ISCA 2011)
  Entry consistency (CMU-TR 1991)

## Slide 19: Related Work – ASM-CMP
Rigel: IEEE Micro 2011
  Differentiates coherent/incoherent
Treadmarks: ISCA 1992
  Twinning and diffing

## Slide 20: Related Work - Alternatives
Reduce directory overhead
  Cuckoo directory (HPCA 2011)
  Tagless directory (MICRO 2009, PACT 2011)
  Waypoint (PACT 2010)
  Region coherence (IEEE Micro 2006)
  SW controlled coherence (…)
Simplify coherence design
  Denovo (PACT 2011)
Coherence is here to stay
  CACM 2012

## Slide 21: Executive Summary & Outline
Acoherent Shared Memory [2012]
  Coherence is complex & inefficient
  Switch to CVS-like checkout/checkin model
  Same performance; less energy for CPUs
Whither Acoherent Shared Memory?
  CPUs coherence “settled”
  GPU/accelerators not ready
  Timing wrong; hard to publish out-there ideas
But seeded Heterogeneous Race Free

## Slide 22: Previous Work
Rerun: ISCA 2008 and CACM 2009
  Race recorder for deterministic replay
  vs. state of the art:
    SAME logging performance, > 10x state reduction
Calvin: HPCA 2011
  Coherence for deterministic execution
    i.e., zero-log-size deterministic replay
  Selective determinism to match program requirements
Hobbes: WoDet 2011
  Strong acoherence in SW runtime

## Slide 23: View from 2012 by Hower
Focus on more specific target system
Stop building new infrastructure!
  Why did I?
    gem5 wasn’t ready
    Started more radical/not clear it would have helped
Step back more often
  Easy to get sucked in to details – usually don’t matter
Functional specification of consistency -> yuck!

## Slide 24: 2012 Thesis Conclusions
Going forward:
  HW designs must find efficiency
  SW will want to see caches/control placement
ASM: viable alternative to coherent shared memory
  Semantic cooperation between HW/SW
ASM-CMP: build components w/o coherence engine
  Make custom integration easier
Practically:
  Will the next x86 core use ASM? No
  Will a heterogeneous accelerator? Maybe

## Slide 25: View from 2015 by Hower & Hill
Did Coherence need to be revisited?
  For CPUs, perhaps “no”
  Solutions complex, but this complexity is “sunk cost”
What about coherence to GPU/accelerators?
  Acoherent Shared Memory might be a good match
  Hower did not have the needed infrastructure for this
  Crude GPU models would have been trashed.
Our timing was wrong
Regrettably hard to publish imperfect visions
Can effect next career steps

## Slide 26: Hower’s Previous Work in 2012
Rerun: ISCA 2008 and CACM 2009
  Race recorder for deterministic replay
  vs. state of the art:
    SAME logging performance, > 10x state reduction
Calvin: HPCA 2011
  Coherence for deterministic execution
    i.e., zero-log-size deterministic replay
  Selective determinism to match program requirements
Hobbes: WoDet 2011
  Strong acoherence in SW runtime

## Slide 27: Heterogeneous-race-free Memory Models
Derek R. Hower, Blake A. Hechtman,
Bradford M. Beckmann, Benedict R. Gaster,
Mark D. Hill, Steven K. Reinhardt, David A. Wood
ASPLOS 3/4/2014

## Slide 28: Heterogeneous SOFTWARE
OpenCL Software Hierarchy
  Sub-group (CUDA Warp)
  Workgroup (thread block)
  NDRange (grid)
  System (system)
Scoped Synchronization
  Sync w.r.t. subset of threads
  OpenCL: flag.store(1,…, memory_scope_work_group)
  CUDA: __threadfence{_block}
Why? See Hardware
hierarchical W/ Scopes
OpenCL Execution Hierarchy

## Slide 29: Heterogeneous HAREWARE
E.g. GPU memory system: Write combining caches
Scopes have different costs:
  Sync w/ work-group: flush write buffer
  Sync w/ NDrange: flush write buffer + L1 cache flush/invalidate
Programming with scoped synchronization?
hierarchical W/ Scopes
L1
L1
L2
WI1
WI2
WI3
WI4
Write buffers:

## Slide 30: Heterogeneous-race-free Memory Models
History
  1979: Sequential Consistency (SC): like multitasking uniprocessor
  1990: SC for DRF: SC for programs that are data-race-free
  2005: Java uses SC for DRF (+ more)
  2008: C++ uses SC for DRF (+ more)
Q: Heterogeneous memory model in < 3 decades?
2014: SC for Heterogeneous-Race-Free: SC for programs
  With “enough” synchronization (DRF)
  Of “enough” scope (HRF)
  Variants for current & future SW/HW
2014: Heterogeneous System Architecture (HSA) ADOPTS!
Already questioned at MICRO’15 

## Slide 31: Heterogeneous-race-free Memory Models
HRF-direct: Synchronization Chains use Same Scope
  thread 1 sync w/ thread 2 sync w/ thread 3
HRF-indirect: Synchronization Chains w/ Different Scope
  thread 1 sync w/ thread 2 sync w/ thread 3
 | HRF-direct | HRF-indirect
Allowed HW Relaxations | Tomorrow’s potential | Today’s implementations
Target Workloads | Today’s regular workloads | Tomorrow’s irregular workloads
Scope Layout Flexibility | Heterogeneous | Hierarchical




## Slide 32
HRF-direct
wi1 wi2 wi3 wi4
ST A = 1
Release_WG1
Acquire_WG1
X = LD A
Release_DEVICE
Acquire_DEVICE
Y = LD A
Work-group WG1
Work-group WG2
Correct synchronization: communicating actors use exact same scope
  Including all stops in transitive chain
Example is a race: Y undefined
The fix: wi1-wi2 use DEVICE scope
wi1, wi3 communicate

## Slide 33
HRF-indirect
wi1 wi2 wi3 wi4
ST A = 1
Release_WG1
Acquire_WG1
X = LD A
Release_DEVICE
Acquire_DEVICE
Y = LD A
Work-group WG1
Work-group WG2
Correct synchronization:
  All paired synchronization uses exact same scope
  Transitive chains OK
Example is a not a race: Y = 1
Paired synchronization
with same scope
Transitive chain
Through wi2

## Slide 34: Executive Summary & Outline
Acoherent Shared Memory [2012]
  Coherence is complex & inefficient
  Switch to CVS-like checkout/checkin model
  Same performance; less energy for CPUs
Whither Acoherent Shared Memory?
  CPUs coherence “settled”
  GPU/accelerators not ready
  Timing wrong; hard to publish out-there ideas
But seeded Heterogeneous Race Free